## Slide 1
L1a
L1b
L2
MSHR
MSHR
MSHR
Read Request
Write Request
Copy-Back
Prefetch
Request | Answer
Find free MSHR Allocate Untreated Answer Low Latency (free package) | Find existing MSHR Set Untreated Answer High Latency (R/W/P Answer)
Find Next Untreated Request Directory->Request(package) | Find Next Untreated Answer Directory->Answer(package)
Dir: package->memory_operation=READ_REQUEST return memory_status=TRANSMIT | Dir: Coherence Answer(package) Coherence Access(package) package->memory_operation=READ_ANSWER Dir->release_lock() return memory_status=TRANSMIT
Find Next Transmit Send Package If Request: Directory->Wait(package) | Find Next Transmit Send Package Free Package
Dir: package->memory_operation=Read Answer return memory_status=wait | 

## Slide 2
Type |  | States Before |  |  | Details | States After |  | 
 |  | L1a | L1b | L2 |  | L1a | L1b | L2
Cache Read | Read Miss L1, Read Miss L2 | I | I | I |  | E | I | E
 |  | I | I | I |  | I | I | E
 | Read Hit L1 | M | - | - |  | M | - | -
 |  | O | - | - |  | O | - | -
 |  | E | - | - |  | E | - | -
 |  | S | - | - |  | S | - | -
 | Read Miss L1, Read Hit L2 | I | M | E |  | S | S | O
 |  | I | O | E |  | S | S | O
 |  | I | E | E |  | S | S | S
 |  | I | S | S |  | S | S | S
 |  | I | I | O |  | S | I | O
 |  | I | I | E |  | E | I | E
 |  | I | I | S |  | S | I | S
Type |  | States Before |  |  | Details | States After |  | 
 |  | L1a | L1b | L2 |  | L1a | L1b | L2
Cache Write | Write Miss L1, Read Miss L2 | I | I | I |  | M | I | E
 |  | I | I | I |  | I | I | E
 | Write Hit L1 | M | - | - |  | M | I | E
 |  | O | - | - |  | M | I | E
 |  | E | - | - |  | M | I | E
 |  | S | - | - |  | M | I | E
 | Write Miss L1, Read Hit L2 | I | M | E |  | M | I | E
 |  | I | O | E |  | M | I | E
 |  | I | E | E |  | M | I | E
 |  | I | S | S |  | M | I | E
 |  | I | I | O |  | M | I | E
 |  | I | I | E |  | M | I | E
 |  | I | I | S |  | M | I | E